# CE444: Geotechnical Design
# Homework Assignment #5

February 6th, 2026

To: Dr. Arash Khosravifar
From: Brandon Auyeung
## Problem 1.
A shallow square footing is being considered as a foundation option to support both gravity and seismic loads for a marquee sign. The footing width is 4-by-4 meters and the embedment depth D = 1.5 meters. The soil deposit includes a saturated clay with undrained shear strength Su = 50 kPa and total unit weight of γ = 17 kN/m3. The water table is very deep. The mass of the marquee sign is approximately m = 100 metric ton (100 Mg). Assume pinned connection between column and foundation (i.e. no bending moment transferred to the foundation).
### Find:
#### Part A
​Determine q_{bL}^{net} .

#### Part B
Determine factor of safety, FS.
### Solution:
#### Part A

## Problem 2.
### Given:
A rectangular footing of width B and length 2B will need to support a vertical dead plus live load of 1.7 MN (including the expected weight of the foundation) with a factor of safety against bearing failure of 2.5. The footing base will be placed 1.4 m below the ground surface in a deep deposit of sand. The water table is at a depth of 20 m. The soil's total unit weight above the water table is 18 kN/m3 and below the water table is 20 kN/m3.
### Find:
#### Part A
Prepare a spreadsheet that computes the minimum footing width (B) required to provide adequate safety against bearing failure
#### Part B
Plot B versus the effective friction angle of the sand (for \phi' values of 30° to 45°).

### Solution:
Constant values of γ = 18 kNm-3, D = 1.4 m, q0 = γD = 25.2 kPa, and F.S. = 2 were used.
The following equations were used to calculate the factors in Table 1.
L = 2B	as given by the problem statement

N_q = \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'} \text{exp}\left[ \pi \text{tan}\phi' \right]

N_\gamma = 1.5(N_q -1) \text{tan}\phi'

\beta = tan^{-1} \left(\frac{Q_h}{Q_v}\right) = tan^{-1}(0) = 0

i_q = \left( 1 - \frac{\beta}{90^\circ}\right)^2 = (1-0)^2 = 1

i_\gamma = \left( 1 - \frac{\beta}{\phi'}\right)^2 = (1-0)^2 = 1

s_q = s_\gamma = 1 + 0.1\frac{B}{L} \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'} = 1 + \frac{0.1}{2} \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'}

d_q = d_\gamma = 1 + 0.1\frac{D}{B} \sqrt{\frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'}} = 1 + 0.1\frac{1.4 \text{m}}{B} \sqrt{\frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'}}

These factors are able to be used to calculate the demand, capacity, and the factor of safety relationship.
(q_{bL}^{net})_C = \frac{1700 \text{kN} }{2B^2} - q_0	Capacity

(q_{bL}^{net})_D= q_0 N_q s_q i_q d_q + \frac{1}{2} \gamma N_\gamma s_\gamma i_\gamma d_\gamma	Demand

\text{F.S.} = {{(q_{bL}^{net})_C}}} \div {{(q_{bL}^{net})_D}} \Rightarrow 0 = (q_{bL}^{net})_C - \text{F.S.} \times (q_{bL}^{net})_D

By setting all variables in the above equation(s) in terms of B and \phi' , the Sympy module in Python can solve the above expression for B for each given value of \phi' from 30 degrees to 45 degrees.

#### Part A

$\begin{tabular}{*{15}{c}} \phi' [\circ] & B [m] & L [m] & N_q & s_q & i_q & d_q & N_{\gamma} & s_{\gamma} & i_{\gamma} & d_{\gamma} & (q_{bL}^{net})_C & (q_{bL}^{net})_D& FS \\ \hline \hline 30 & 1.511454 & 3.022908 & 18.401122 & 1.150000 & 1 & 1.160433 & 15.069814 & 1.150000 & 1 & 1.160433 & 867.184461 & 346.873784 & 2.5 \\ \hline 31& 1.422017 & 2.844034 & 20.630793 & 1.156202 & 1 & 1.174013 & 17.693056 & 1.156202 & 1 & 1.174013 & 987.871092 & 395.148437 & 2.5\\ \hline 32& 1.335853 & 2.671707 & 23.176776 & 1.162729 & 1 & 1.189068 & 20.786382 & 1.162729 & 1 & 1.189068 & 1127.806888 & 451.122755 & 2.5\\ \hline 33& 1.252857 & 2.505714 & 26.092012 & 1.169606 & 1 & 1.205808 & 24.442415 & 1.169606 & 1 & 1.205808 & 1290.804155 & 516.321662 & 2.5\\ \hline 34& 1.172928 & 2.345855 & 29.439792 & 1.176857 & 1 & 1.224482 & 28.774323 & 1.176857 & 1 & 1.224482 & 1481.601535 & 592.640614 & 2.5\\ \hline 35& 1.095971 & 2.191942 & 33.296091 & 1.184509 & 1 & 1.245387 & 33.920950 & 1.184509 & 1 & 1.245387 & 1706.134162 & 682.453665 & 2.5\\ \hline 36& 1.021900 & 2.043799 & 37.752497 & 1.192592 & 1 & 1.268877 & 40.053378 & 1.192592 & 1 & 1.268877 & 1971.896747 & 788.758699 & 2.5\\ \hline 37& 0.950633 & 1.901266 & 42.919912 & 1.201140 & 1 & 1.295379 & 47.383379 & 1.201140 & 1 & 1.295379 & 2288.436718 & 915.374687 & 2.5\\ \hline 38& 0.882097 & 1.764193 & 48.933253 & 1.210187 & 1 & 1.325409 & 56.174342 & 1.210187 & 1 & 1.325409 & 2668.031587 & 1067.212635 & 2.5\\ \hline 39& 0.816224 & 1.632448 & 55.957459 & 1.219775 & 1 & 1.359602 & 66.755509 & 1.219775 & 1 & 1.359602 & 3126.630559 & 1250.652224 & 2.5\\ \hline 40& 0.752955 & 1.505911 & 64.195206 & 1.229945 & 1 & 1.398737 & 79.540612 & 1.229945 & 1 & 1.398737 & 3685.180332 & 1474.072133 & 2.5\\ \hline 41& 0.692239 & 1.384479 & 73.896891 & 1.240748 & 1 & 1.443780 & 95.052451 & 1.240748 & 1 & 1.443780 & 4371.517537 & 1748.607015 & 2.5\\ \hline 42& 0.634032 & 1.268065 & 85.373623 & 1.252234 & 1 & 1.495945 & 113.955527 & 1.252234 & 1 & 1.495945 & 5223.109785 & 2089.243914 & 2.5\\ \hline 43& 0.578300 & 1.156599 & 99.014259 & 1.264464 & 1 & 1.556767 & 137.099663 & 1.264464 & 1 & 1.556767 & 6291.088403 & 2516.435361 & 2.5\\ \hline 44& 0.525016 & 1.050032 & 115.307902 & 1.277502 & 1 & 1.628208 & 165.578787 & 1.277502 & 1 & 1.628208 & 7646.281582 & 3058.512633 & 2.5\\ \hline 45& 0.474167 & 0.948334 & 134.873841 & 1.291421 & 1 & 1.712808 & 200.810761 & 1.291421 & 1 & 1.712808 & 9388.402998 & 3755.361199 & 2.5\\ \hline \end{tabular}$

Table 1. Prepared spreadsheet of values used to find B given a FS = 2.5 and a variable effective friction angle of sands.
#### Part B
Figure 1. Required foundation width to achieve a 2.5 factor of safety with respect to effective friction angle of sand.