# CE444: Geotechnical Design
# Homework Assignment #5

March 6th, 2026

To: Dr. Arash Khosravifar
From: Brandon Auyeung
## Problem 1.
A shallow square footing is being considered as a foundation option to support both gravity and seismic loads for a marquee sign. The footing width is 4-by-4 meters and the embedment depth D = 1.5 meters. The soil deposit includes a saturated clay with undrained shear strength Su = 50 kPa and total unit weight of γ = 17 kN/m3. The water table is very deep. The mass of the marquee sign is approximately m = 100 metric ton (100 Mg). Assume pinned connection between column and foundation (i.e. no bending moment transferred to the foundation).
### Find:
#### Part A
​Determine q_{bL}^{net} .

#### Part B
Determine factor of safety, FS.
### Solution:
#### Part A
The equation to determine q_{bL}^{net} is as follows.

q_{bL}^{net} = S_u N_c s_c i_c d_c + q_0 N_q - q_0

To get the factors to determine q_{bL}^{net} , the following equations were used.

N_c = 2 + \pi

s_c = 1+0.2 \frac{B}{L} = 1.2	Square Footing; B = L

i_c = 1 - 1.3 \frac{Q_h}{Q_v} = 1 - 1.3 \frac{438.5 \ \text{kN}}{981 \ \text{kN}} = 0.419	Ignore \frac{Q_h}{Q_v} \leq 0.4 condition.

d_c = 1 + 0.2 \frac{D}{B} = 1 +0.2 \frac{1.5 \ \text{m}}{4 \ \text{m}} = 1.075

N_q = 1	Clay

q_0 = D_f \gamma = 1.5 \text{m} \times 17 \text{kNm}^{-3} = 25.5 \ \text{kPa}

Given the value of Su, we can calculate q_{bL}^{net} .

q_{bL}^{net} = 50 \ \text{kPa} (2 + \pi) (1.2) (0.419) (1.075) + 25.5 \ \text{kPa} (1) - 25.5 \ \text{kPa}

q_{bL}^{net} = 137.8 \ \text{kPa}

#### Part B
The factor of safety is calculated as follows.
\text{F.S.} = \frac{q_{bL}^{net}}{q^{net}}

To calculate qnet, the following equation is used.
q^{net} = \frac{Q_v}{B^2} - q_0 = \frac{981 \ \text{kN}}{(4 \ \text{m})^2} - 25.5 \ \text{kPa} = 35.8 \ \text{kPa}

The value of the factor of safety can now be determined.
\text{F.S.} = \frac{q_{bL}^{net}}{q^{net}} = \frac{137.8 \ \text{kPa}}{35.8 \ \text{kPa}} = 3.8

## Problem 2.
### Given:
A rectangular footing of width B and length 2B will need to support a vertical dead plus live load of 1.7 MN (including the expected weight of the foundation) with a factor of safety against bearing failure of 2.5. The footing base will be placed 1.4 m below the ground surface in a deep deposit of sand. The water table is at a depth of 20 m. The soil's total unit weight above the water table is 18 kN/m3 and below the water table is 20 kN/m3.
### Find:
#### Part A
Prepare a spreadsheet that computes the minimum footing width (B) required to provide adequate safety against bearing failure
#### Part B
Plot B versus the effective friction angle of the sand (for \phi' values of 30° to 45°).

### Solution:
Constant values of γ = 18 kNm-3, D = 1.4 m, q0 = γD = 25.2 kPa, and F.S. = 2 were used.
The following equations were used to calculate the factors in Table 1.
L = 2B	as given by the problem statement

N_q = \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'} \text{exp}\left[ \pi \text{tan}\phi' \right]

N_\gamma = 1.5(N_q -1) \text{tan}\phi'

\beta = tan^{-1} \left(\frac{Q_h}{Q_v}\right) = tan^{-1}(0) = 0

i_q = \left( 1 - \frac{\beta}{90^\circ}\right)^2 = (1-0)^2 = 1

i_\gamma = \left( 1 - \frac{\beta}{\phi'}\right)^2 = (1-0)^2 = 1

s_q = s_\gamma = 1 + 0.1\frac{B}{L} \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'} = 1 + \frac{0.1}{2} \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'}

d_q = d_\gamma = 1 + 0.1\frac{D}{B} \sqrt{\frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'}} = 1 + 0.1\frac{1.4 \text{m}}{B} \sqrt{\frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'}}

These factors are able to be used to calculate the demand, capacity, and the factor of safety relationship.
q^{net} = \frac{1700 \text{kN} }{2B^2} - q_0	Demand

q_{bL}^{net}= q_0 N_q s_q i_q d_q + \frac{1}{2} \gamma N_\gamma s_\gamma i_\gamma d_\gamma - q_0	Capacity

\text{F.S.} = \frac{q_{bL}^{net}}{q^{net}} \Rightarrow 0 = q_{bL}^{net} - \text{F.S.} q^{net}

By setting all variables in the above equation(s) in terms of B and \phi' , the Sympy module in Python can solve the above expression for B for each given value of \phi' from 30 degrees to 45 degrees.

#### Part A

$\begin{tabular}{*{15}{c}} \phi' [\circ] & B [m] & L [m] & N_q & s_q & i_q & d_q & N_{\gamma} & s_{\gamma} & i_{\gamma} & d_{\gamma} & q_{bL}^{net} \text{[kPa]} & q^{net} \text{[kPa]} & FS \\ \hline \hline 30 & 1.511454 & 3.022908 & 18.401122 & 1.150000 & 1 & 1.160433 & 15.069814 & 1.150000 & 1 & 1.160433 & 867.184461 & 346.873784 & 2.5 \\ \hline 31& 1.422017 & 2.844034 & 20.630793 & 1.156202 & 1 & 1.174013 & 17.693056 & 1.156202 & 1 & 1.174013 & 987.871092 & 395.148437 & 2.5\\ \hline 32& 1.335853 & 2.671707 & 23.176776 & 1.162729 & 1 & 1.189068 & 20.786382 & 1.162729 & 1 & 1.189068 & 1127.806888 & 451.122755 & 2.5\\ \hline 33& 1.252857 & 2.505714 & 26.092012 & 1.169606 & 1 & 1.205808 & 24.442415 & 1.169606 & 1 & 1.205808 & 1290.804155 & 516.321662 & 2.5\\ \hline 34& 1.172928 & 2.345855 & 29.439792 & 1.176857 & 1 & 1.224482 & 28.774323 & 1.176857 & 1 & 1.224482 & 1481.601535 & 592.640614 & 2.5\\ \hline 35& 1.095971 & 2.191942 & 33.296091 & 1.184509 & 1 & 1.245387 & 33.920950 & 1.184509 & 1 & 1.245387 & 1706.134162 & 682.453665 & 2.5\\ \hline 36& 1.021900 & 2.043799 & 37.752497 & 1.192592 & 1 & 1.268877 & 40.053378 & 1.192592 & 1 & 1.268877 & 1971.896747 & 788.758699 & 2.5\\ \hline 37& 0.950633 & 1.901266 & 42.919912 & 1.201140 & 1 & 1.295379 & 47.383379 & 1.201140 & 1 & 1.295379 & 2288.436718 & 915.374687 & 2.5\\ \hline 38& 0.882097 & 1.764193 & 48.933253 & 1.210187 & 1 & 1.325409 & 56.174342 & 1.210187 & 1 & 1.325409 & 2668.031587 & 1067.212635 & 2.5\\ \hline 39& 0.816224 & 1.632448 & 55.957459 & 1.219775 & 1 & 1.359602 & 66.755509 & 1.219775 & 1 & 1.359602 & 3126.630559 & 1250.652224 & 2.5\\ \hline 40& 0.752955 & 1.505911 & 64.195206 & 1.229945 & 1 & 1.398737 & 79.540612 & 1.229945 & 1 & 1.398737 & 3685.180332 & 1474.072133 & 2.5\\ \hline 41& 0.692239 & 1.384479 & 73.896891 & 1.240748 & 1 & 1.443780 & 95.052451 & 1.240748 & 1 & 1.443780 & 4371.517537 & 1748.607015 & 2.5\\ \hline 42& 0.634032 & 1.268065 & 85.373623 & 1.252234 & 1 & 1.495945 & 113.955527 & 1.252234 & 1 & 1.495945 & 5223.109785 & 2089.243914 & 2.5\\ \hline 43& 0.578300 & 1.156599 & 99.014259 & 1.264464 & 1 & 1.556767 & 137.099663 & 1.264464 & 1 & 1.556767 & 6291.088403 & 2516.435361 & 2.5\\ \hline 44& 0.525016 & 1.050032 & 115.307902 & 1.277502 & 1 & 1.628208 & 165.578787 & 1.277502 & 1 & 1.628208 & 7646.281582 & 3058.512633 & 2.5\\ \hline 45& 0.474167 & 0.948334 & 134.873841 & 1.291421 & 1 & 1.712808 & 200.810761 & 1.291421 & 1 & 1.712808 & 9388.402998 & 3755.361199 & 2.5\\ \hline \end{tabular}$

Table 1. Prepared spreadsheet of values used to find B given a FS = 2.5 and a variable effective friction angle of sands.
#### Part B

Figure 1. Required foundation width to achieve a 2.5 factor of safety with respect to effective friction angle of sand.
## Problem 3.
### Given:
Square footings of width B will support columns for an elevated bridge that crosses over a park that periodically floods during winter. The footings will be embedded a depth Df in a deep deposit of medium-dense gravelly sand having an effective friction angle of 35 degrees. The water level can rise to about 5 feet over the ground surface. The unit weight of the gravelly sand is about 128 pcf when saturated. The design dead plus live loads imposed on each footing are a vertical load of 320 kips (along the centerline of the footing), a horizontal load of 60 kips (at the column base), and an overturning moment of 180 kip⋅ft (in one direction only).
### Find:
Perform all calculations in SI units.
#### Part A
Determine the minimum footing width B required to provide a factor of safety against bearing failure of 3.0 for embedment depths (D) ranging from 1 to 6 feet.
#### Part B
Plot the minimum B versus D.
### Solution:
#### Part A
Constant soil parameter values of γ’ = 10.3 kNm-3, \phi' = 35 ^ \circ , and F.S. = 3 were used. Constant load values of Qv = 1423.3 kN, Qh = 266.9 kN, and ML = 244.0 kNm were used.

The eccentricity, e, was calculated as follows.
e = \frac{M_L}{Q_v} = \frac{244.0 \text{kNm}}{1423.4 \text{kN}} = 0.17 \text{m}

The following equations were used to calculate the factors in Table 2.
L_{eff} = B

B_{eff} = B - 2e = B - 2(0.17 \ \text{m}) = B - 0.34 \ \text{m}

\beta = tan^{-1} \left(\frac{Q_h}{Q_v}\right) = tan^{-1}\left(\frac{266.9 \text{kN}}{1423.4 \text{kN}}\right) = 10.6^\circ

N_q = \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'} \text{exp}\left[ \pi \text{tan}\phi' \right] = \frac{1 + \text{sin}35^\circ}{1 - \text{sin}35^\circ} \text{exp}\left[ \pi \text{tan}35^\circ \right] = 33.3

i_q = \left( 1 - \frac{\beta}{90^\circ}\right)^2 = (1-\frac{10.6^\circ}{90^\circ})^2 = 0.778

N_\gamma = 1.5(N_q -1) \text{tan}\phi' = 1.5 (33.3 - 1) \text{tan} 35^\circ = 33.9

i_\gamma = \left( 1 - \frac{\beta}{\phi'}\right)^2 = (1-\frac{10.6^\circ}{35^\circ})^2 = 0.485

q_0' = \gamma ' D = 10.3 \text{kNm}^{-3} D

s_q = s_\gamma = 1 + 0.1\frac{B}{L} \frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'} = 1 + 0.1 \ \frac{B - 0.34 \ \text{m}}{B} \frac{1 + \text{sin}35^\circ}{1 - \text{sin}35^\circ}

d_q = d_\gamma = 1 + 0.1\frac{D}{B} \sqrt{\frac{1 + \text{sin}\phi'}{1 - \text{sin}\phi'}} = 1 + 0.1 \frac{D}{B} \sqrt{\frac{1 + \text{sin}35^\circ}{1 - \text{sin}35^\circ}}

These factors are able to be used to calculate the demand, capacity, and the factor of safety relationship.
q^{net} = \frac{Q_v}{B_{eff} L_{eff} } - q_0'	Demand

q_{bL}^{net}= q_0' N_q s_q i_q d_q + \frac{1}{2} \gamma N_\gamma s_\gamma i_\gamma d_\gamma - q_0'	Capacity

\text{F.S.} = \frac{q_{bL}^{net}}{q^{net}} \Rightarrow 0 = q_{bL}^{net} - \text{F.S.} q^{net}

By setting all variables in the above equation(s) in terms of B and D, the Sympy module in Python can solve the above expression for B for each given value of D from 1 foot to 6 feet (i.e. 0.3048 m to 1.8288 m).

\begin{tabular}{*{15}{c}} D \ \text{[m]}& q_0 \ \text{[kPa]} & N_q & s_q & i_q & d_q & N_\gamma & s_\gamma & i_\gamma & d_\gamma & B \ \text{[m]} & B_{eff} \ \text{[m]}& L \ \text{[m]} & q_{bL}^{net} \ \text{[kPa]}& q^{net} \ \text{[kPa]}\\ \hline \hline 0.304800 & 3.139177 & 33.296091 & 1.330114 & 0.777931 & 1.020124 & 33.920950 & 1.330114 & 0.485225 & 1.020124 & 3.252451 & 2.909568 & 3.252451 & 441.811102 & 147.270367 \\ \hline 0.609600 & 6.278354 & 33.296091 & 1.326439 & 0.777931 & 1.044546 & 33.920950 & 1.326439 & 0.485225 & 1.044546 & 2.971724 & 2.628841 & 2.971724 & 527.756773 & 175.918924 \\ \hline 0.914400 & 9.417531 & 33.296091 & 1.322743 & 0.777931 & 1.073450 & 33.920950 & 1.322743 & 0.485225 & 1.073450 & 2.734353 & 2.391469 & 2.734353 & 624.752602 & 208.250867 \\ \hline 1.219200 & 12.556708 & 33.296091 & 1.319030 & 0.777931 & 1.107024 & 33.920950 & 1.319030 & 0.485225 & 1.107024 & 2.531242 & 2.188359 & 2.531242 & 733.204376 & 244.401459 \\ \hline 1.524000 & 15.695885 & 33.296091 & 1.315295 & 0.777931 & 1.145477 & 33.920950 & 1.315295 & 0.485225 & 1.145477 & 2.355278 & 2.012394 & 2.355278 & 853.821101 & 284.607034 \\ \hline 1.828800 & 18.835062 & 33.296091 & 1.311530 & 0.777931 & 1.189067 & 33.920950 & 1.311530 & 0.485225 & 1.189067 & 2.200999 & 1.858115 & 2.200999 & 987.598397 & 329.199466 \\ \hline \end{tabular}

Table 2. Prepared spreadsheet of values used to find B given a FS = 2.5 and a variable embedded depth of foundation.
#### Part B
Figure 2. Required foundation width to achieve a 3 factor of safety with respect to embedded depth of foundation.